## Slide 1: What Is the Internet?
A network of networks, joining many government, university and private computers together and providing an infrastructure for the use of E-mail, bulletin boards, file archives, hypertext documents, databases and other computational resources
The vast collection of computer networks which form and act as a single huge network for transport of data and messages across distances which can be anywhere from the same office to anywhere in the world.
Written by William F. Slater, III
1996
President of the Chicago Chapter of the Internet Society
Copyright 2002, William F. Slater, III, Chicago, IL, USA
ghjgjghjghj
Notes: 5

## Slide 2: What is the Internet?
The largest network of networks in the world.
Uses TCP/IP protocols and packet switching .
Runs on any communications substrate.
From Dr. Vinton Cerf,
Co-Creator of TCP/IP

## Slide 3: Brief History of the Internet
1968 - DARPA (Defense Advanced Research Projects Agency) contracts with BBN (Bolt, Beranek & Newman) to create ARPAnet
1970 - First five nodes:
  UCLA
  Stanford
  UC Santa Barbara
  U of Utah, and
  BBN
1974 - TCP specification by Vint Cerf
1984 – On January 1, the Internet with its 1000 hosts converts en masse to using TCP/IP for its messaging

## Slide 4: Internet Growth Trends
1977: 111 hosts on Internet hjhjk,njkh
1981: 213 hosts
1983: 562 hosts
1984: 1,000 hosts
1986: 5,000 hosts
1987: 10,000 hosts
1989: 100,000 hosts
1992: 1,000,000 hosts
2001: 150 – 175 million hosts
2002: over 200 million hosts
By 2010, about 80% of the planet will be on the Internet

## Slide 5: No. of Participating Hosts Oct. ‘90 - Apr. ‘98

## Slide 6
The Internet was not known as "The Internet" until January 1984, at which time
there were 1000 hosts that were all converted over to using TCP/IP.
Chart by William F. Slater, III
Sept. 1, 2002
Dot-Com Bust Begins
Copyright 2002, William F. Slater, III, Chicago, IL, USA

## Slide 7: Domain Name Registration Jan. ‘89 - Jul. ‘97
April 2001: 31,000,000 Domain Names!!!

## Slide 8: TCP/IP Addresses
Every host on the Internet must have a unique IP address
The IP address is a 32-bit number which we write in dotted decimal notation
The first part of the IP address is the network address – the remainder is the host ID
A subnet mask is used to determine the network address from a IP host address
All hosts on the same network are configured with the same subnet mask

## Slide 9: Network Address Example
Host address: 192.252.12.14
Subnet mask: 255.255.255.0
11000000.11111100.00001100.00001110
11111111.11111111.11111111.00000000
11000000.11111100.00001100.00000000
To obtain the network address, AND the host IP with its subnet mask:
Host IP:
Mask:
Net addr:
which is:
192.152.12.0

## Slide 10: Obtaining an Internet Network Address
IP network addresses must be unique, or the Internet will not be stable
The Internet Network Information Centre (InterNIC) was originally responsible for issuing Internet network addresses
Today, the Internet Assigned Number Authority (IANA) issues network addresses to Information Service Providers (ISPs)
ISPs split networks up into subnets and sell them on to their customers

## Slide 11: Domain Name System (DNS)
IP addresses are used to identify hosts on a TCP/IP network
Example: 134.220.1.9
Numbers are not ‘friendly’ – people prefer names
DNS is a protocol used to map IP addresses to textual names
E.g. www.wlv.ac.uk maps to 134.220.1.9

## Slide 12: DNS on the Internet
DNS names have a hierarchical structure
Example: www.wlv.ac.uk
com
net
fr
uk
us
Root Level
ac
co
aston
wlv
staffs
ftp
www
clun
Top-level domain
Second-level
domain
Server name

## Slide 13: Internet Email Addresses
The Local part is the name of a special file stored on the mail server called the user’s mailbox
The Domain name is resolved using DNS
The mail server is also known as a mail exchanger
Local part
Domain name of mail server
@
mel.ralph@wlv.ac.uk

## Slide 14: Hypertext Transfer Protocol (HTTP)
HTTP is the protocol used to access resources on the World Wide Web
A browser application is used to send a request to the WWW server for a resource, e.g. a web page, graphics file, audio file, etc.
The server responds by sending the resource (a file) to the client and closing the connection
Request
Browser app
WWW server
The Internet
(TCP/IP)
Web page

## Slide 15: Uniform Resource Locator (URL)
URL is the standard for specifying the whereabouts of a resource (such as a web page) on the Internet
A URL has four parts:
  The protocol used to retrieve the resource
  The host where the resource is held
  The port number of the server process on the host
  The name of the resource file
http://www.wlv.ac.uk:80/index.html
Protocol
Host
Port number
Name of web page

## Slide 16: URL Defaults
A server will normally be setup to use standard defaults
This enables the URL to be simplified
In the case of a Web server for example
  Default port will be 80
  Default name for home page will be index.html
Hence the previous URL can be shortened to
http://www.wlv.ac.uk/

## Slide 17: File Transfer Protocol (FTP)
Protocol for copying files between client and an FTP server
Uses a TCP connection for reliable transfer of files with error-checking
Most browsers support FTP, or you can use a dedicated FTP client program, e.g WS_FTP
Trivial File Transfer Protocol (TFTP) is a lightweight version for small memory devices
ftp://ftp.demon.co.uk/pub/

## Slide 18: Telnet
Telnet allows a user to run commands and programs remotely on another computer across the Internet
The user runs a Telnet client program on the local host
A Telnet server process must be running on the remote host
The user must have the necessary permissions and password to access the remote host

## Slide 19: Some Port Assignments
21 FTP
23 Telnet
25 smtp (mail)
70 gopher
79 finger
80 HTTP